## Slide 1
CEE 370
Intersection Simulator
Academic presentation on the problem, methodology, simulation design, results, and future work.
Project context
Browser-based signalized intersection simulator for teaching traffic operations and control concepts.
Prepared for
Transportation Fundamentals
Author
Dr. Kun Xie, Old Dominion University
Intersection Simulator | Generated from local project files and reproducible scenario analysis

## Slide 2
Problem And Motivation
Why this simulator matters in a transportation fundamentals setting
Core Problem
Students often learn signal timing, queueing, and delay from equations alone, without seeing the operational consequences in real time.
A compact classroom simulator can connect traffic engineering theory to observable system behavior at a four-leg signalized intersection.
The project is intended for concept exploration and instruction rather than high-fidelity field calibration.
Guiding Question
How do signal timing, arrival randomness, turning behavior, and vehicle mix influence queue formation and delay?
Project Scope
One inbound lane per approach
Two-phase signal control
User-adjustable demand and traffic composition
Live metrics for arrivals, departures, queue, and delay
Teaching focus: visualization, experimentation, and interpretation of traffic operations

## Slide 3
Methodology
How the simulator translates engineering assumptions into dynamic system behavior
1. Define Inputs
Signal timings, arrival rates by approach, free-flow speed, left-turn ratio, large-vehicle ratio, and simulation speed.
2. Generate Demand
Vehicle arrivals are sampled stochastically for each approach, creating natural variability in queue growth.
3. Update Signals
The controller alternates east-west and north-south phases with adjustable yellow clearance intervals.
4. Move Vehicles
Vehicles follow lane-based trajectories, obey car-following logic, and check permissive left-turn conflicts.
5. Compute Metrics
The simulator continuously reports queue counts, average queue, maximum queue, and average delay.
Methodological emphasis: simple enough for classroom use, but rich enough to show the interaction between control, demand, and vehicle behavior.
Model class: interactive teaching simulator with stochastic arrivals and simplified operational logic

## Slide 4
Simulation Design
Geometry, control structure, and performance outputs represented in the application
Intersection Layout
EB
WB
SB
NB
Component Architecture
User Inputs
Signal Logic
Vehicle Generation
Movement + Yield
Performance Metrics
Outputs shown in the interface include arrivals, departures, current queue, average queue, maximum queue, and average delay.
Design intent: expose the major mechanisms of signalized intersection operation without unnecessary software complexity

## Slide 5
Results
Illustrative scenario analysis generated from the simulator logic
Baseline Avg Delay
50.6 s/veh
Baseline Avg Queue
14.7 veh
Baseline Max Queue
31.5 veh
Baseline Throughput
1569.6 veh/h
Chart: s/veh
| A: Balanced Demand | B: East-West Heavy Demand | C: East-West Heavy Demand With Retiming
Average Delay (s/veh) | 50.6 | 56.1 | 53.2
Chart: vehicles
| A: Balanced Demand | B: East-West Heavy Demand | C: East-West Heavy Demand With Retiming
Maximum Queue (veh) | 31.5 | 32.8 | 34.6
Scenario | Timing (EW-Y-NS) | Demand (veh/h) | Avg Delay | Throughput
A: Balanced Demand | 30-5-30 | EW 500/500, NS 500/500 | 50.6 s | 1569.6 veh/h
B: East-West Heavy Demand | 30-5-30 | EW 750/750, NS 350/350 | 56.1 s | 1515 veh/h
C: East-West Heavy Demand With Retiming | 40-5-20 | EW 750/750, NS 350/350 | 53.2 s | 1615.5 veh/h
Ten replications per scenario over 1,200 simulated seconds. Results are illustrative and intended for instructional interpretation.

## Slide 6
Interpretation
What the scenario results suggest about system behavior
Under balanced demand, the default 30-5-30 timing produces moderate queues and delay, which is appropriate for classroom demonstration of stable operations.
When east-west demand is increased without retiming, delay and queue growth rise noticeably, showing the sensitivity of performance to volume imbalance.
Reallocating green time to a 40-5-20 split reduces average delay from 56.1 to 53.2 s/veh under the heavy east-west case.
The simulator therefore supports comparative reasoning about timing plans, not just passive visualization.
Key Academic Takeaways
Signal timing affects both queue accumulation and experienced delay.
Random arrivals create run-to-run variation, so replication matters.
Permissive left turns introduce interaction effects beyond simple green-red control.
The tool is best used to teach mechanisms and comparative trends.
Interpretation focus: relative differences and operational insight rather than field calibration

## Slide 7
Future Work
Logical extensions for stronger analytical realism and classroom value
Model Enhancements
Add protected left-turn phasing and additional lane groups.
Represent pedestrian calls and more detailed clearance logic.
Introduce approach-specific turning proportions and heavy-vehicle effects.
Validation And Analysis
Calibrate selected parameters against observed field data.
Add automated batch experiments, confidence intervals, and exportable reports.
Compare simulated measures with deterministic HCM-style calculations.
Instructional Features
Save and reload classroom scenarios for lab exercises.
Add guided experiments that connect inputs to expected hypotheses.
Provide richer visual diagnostics such as phase timelines and queue heatmaps.
Overall direction: preserve the simulator’s accessibility while increasing its analytical depth and instructional flexibility.
Future work balances usability, realism, and educational impact